## Slide 1: Register Allocation: Linear Scan
Compiler
Baojian Hua
bjhua@ustc.edu.cn

## Slide 2: Middle and Back End
AST
translation
IR1
asm
other IR and translation
translation
IR2

## Slide 3: Back-end Structure
IR
TempMap
instruction selector
register allocator
Assem
Assem
instruction scheduler

## Slide 4: Instruction Selection
long f(long x, long y){
long a;
long b;
long c;
long d;
a = x + y;
b = a + 4;
c = b * 2;
d = c / 8;
return d;
}
Positions for x, y, a, b, c, d have NOT be determined at this phase.
long f(long x, long y){
long a, b, c, d;
movq %rdi, x
movq %rsi, y
movq x, a
addq y, a
movq a, b
addq $4, b
movq b, %rax
imulq $2
movq %rax, c
movq c, %rax
cqto
idivq $8
movq %rax, d
movq d, %rax
ret
}

## Slide 5: Register allocation
After instruction selection, instructions still contain variables
  RA goal: put as many as possible of these variables into registers
    speed!
  Spill to memory, only if registers are out of supply
This process is called register allocation
  the most important optimization in modern compilers

## Slide 6: Register Allocation
// code rewriting:
long f(long x, long y){
long a, b, c, d;
movq %rdi, %rdi
movq %rsi, %rsi
movq %rdi, %rax
addq %rsi, %rax
movl %rax, %rax
addl $4, %rax
movq %rax, %rax
imulq $2
movq %rax, %rax
movq %rax, %rax
cqto
idivq $8
movq %rax, %rax
movq %rax, %rax
ret
}
Suppose that the
register allocator
determines that (we
will discuss how to
do this a little
later):
x => %rdi
y => %rsi
a => %rax
b => %rax
c => %rax
d => %rax
(this data structure
is called a temp map)

## Slide 7: Peep-hole Optimization
// code removal:
long f(long x, long y){
long a,b,c,d;
movq %rdi, %rdi
movq %rsi, %rsi
movq %rdi, %rax
addq %rsi, %rax
movl %rax, %rax
addl $4, %rax
movq %rax, %rax
imulq $2
movq %rax, %rax
movq %rax, %rax
cqto
idivq $8
movq %rax, %rax
movq %rax, %rax
ret
}
Peep-hole optimizations try to improve the code by examining the code w.r.t. a sliding window. It is of a local manner.
For example, we can use a code window of width 1, to eliminate the obvious redundancy of the form:
movq r, r

## Slide 8: Assembly
// Optimized function:
long f(long x, long y){
long a, b, c, d;
movq %rdi, %rax
addq %rsi, %rax
addl $4, %rax
imulq $2
cqto
idivq $8
ret
}
long f(long x, long y){
long a;
long b;
long c;
long d;
a = x + y;
b = a + 4;
c = b * 2;
d = c / 8;
return d;
}

## Slide 9: Prologue and Epilogue
// Add pro- and epilogue:
// (do we really need this?)
long f(long x, long y){
pushq %rbp
movq %rsp, %rbp
movq %rdi, %rax
addq %rsi, %rax
addl $4, %rax
imulq $2
cqto
idivq $8
leave
ret
}
long f(long x, long y){
long a;
long b;
long c;
long d;
a = x + y;
b = a + 4;
c = b * 2;
d = c / 8;
return d;
}

## Slide 10: Final Assembly
.text
.globl f
f:
pushq %rbp
movq %rsp, %rbp
movq %rdi, %rax
addq %rsi, %rax
addl $4, %rax
imulq $2
cqto
idivq $8
leave
ret
long f(long x, long y){
long a;
long b;
long c;
long d;
a = x + y;
b = a + 4;
c = b * 2;
d = c / 8;
return d;
}

## Slide 11: Register Allocation
long f(long x, long y){
long a, b, c, d;
movq %rdi, x
movq %rsi, y
movq x, a
addq y, a
movq a, b
addq $4, b
movq b, %rax
imulq $2
movq %rax, c
movq c, %rax
cqto
idivq $8
movq %rax, d
movq d, %rax
ret
}
Register allocation
determines a temp map:
x => %rdi
y => %rsi
a => %rax
b => %rax
c => %rax
d => %rax
How to generate such a temp map?
Key observation: two variables can reside in one register, iff they do NOT live simultaneously.

## Slide 12: Liveness Analysis
long f(long x, long y){
long a, b, c, d;
movq %rdi, x
movq %rsi, y
movq x, a
addq y, a
movq a, b
addq $4, b
movq b, %rax
imulq $2
movq %rax, c
movq c, %rax
cqto
idivq $8
movq %rax, d
movq d, %rax
ret
}
So, we can perform liveness analysis to calculate the live variable information.
On the right, we mark, between adjacent statements, the liveOut set.
{%rax}
{%rax}
{d}
{%rax}
{…}

## Slide 13: Linear Scan Register Allocation
A relatively new allocation based on the notion of live intervals
  [POLETTO et al. 1999]
It is simple, lightweight, fast, and easier to engineering
  (variants) widely used in many production compilers prioritizing compiling speed
    e.g., JIT

## Slide 14
Liveness Intervals

## Slide 15: Motivation: Live Intervals
a = 1
b = 2
c = a+b
d = a+c
e = a+b
f = d+e
a
b
d
e
c
Liveness analysis will specify, for each variable x, its liveness interval
[from, to]
where from and to are its earliest and latest live statements, respectively.

## Slide 16: Or More Precisely
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
Liveness analysis will specify, for each variable x, its liveness interval
[from, to]
where from and to are its earliest and latest live statements, respectively.
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]

## Slide 17: Linear Scan
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
Hence, we can perform a linear scan of these live intervals:
when a new internal starts, allocate an available register to it;
when an exiting interval finishes, evicts its occupying register.
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]

## Slide 18: Linear Scan
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
Suppose we have three registers:
r1, r2, r3.
Encounter variable a: allocate to r1

## Slide 19: Linear Scan
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
Suppose we have three registers:
r1, r2, r3.
Encounter variable a: allocate to r1
Encounter variable b: allocate to r2

## Slide 20: Linear Scan
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
Suppose we have three registers:
r1, r2, r3.
Encounter variable a: allocate to r1
Encounter variable b: allocate to r2
Encounter variable c: allocate to r3

## Slide 21: Linear Scan
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
Suppose we have three registers:
r1, r2, r3.
Encounter variable a: allocate to r1
Encounter variable b: allocate to r2
Encounter variable c: allocate to r3
Evict variable c: recycle r3

## Slide 22: Linear Scan
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
Suppose we have three registers:
r1, r2, r3.
Encounter variable a: allocate to r1
Encounter variable b: allocate to r2
Encounter variable c: allocate to r3
Evict variable c: recycle r3
Encounter variable d: allocate to r3

## Slide 23: Linear Scan
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
Suppose we have three registers:
r1, r2, r3.
Encounter variable a: allocate to r1
Encounter variable b: allocate to r2
Encounter variable c: allocate to r3
Evict variable c: recycle r3
Encounter variable d: allocate to r3
Evict variable a, b: recycle r1 and r2

## Slide 24: Linear Scan
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
Suppose we have three registers:
r1, r2, r3.
Encounter variable a: allocate to r1
Encounter variable b: allocate to r2
Encounter variable c: allocate to r3
Evict variable c: recycle r3
Encounter variable d: allocate to r3
Evict variable a, b: recycle r1 and r2
Encounter variable e: allocate to r1

## Slide 25: Linear Scan
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
Suppose we have three registers:
r1, r2, r3.
Encounter variable a: allocate to r1
Encounter variable b: allocate to r2
Encounter variable c: allocate to r3
Evict variable c: recycle r3
Encounter variable d: allocate to r3
Evict variable a, b: recycle r1 and r2
Encounter variable e: allocate to r1
Evict all registers, when scan finished!

## Slide 26: Linear Scan
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
The result temp map:
a => r1
b => r2
c => r3
d => r3
e => r1

## Slide 27: Linear Scan Algorithm
linearScan(p)
calculate_liveness(p);
build_live_interval(p);
foreach(interval [l, h], in increasing ”l”)
evict(l);
r = allocateOneReg(allRegs);
allocate([l, h] to r);

## Slide 28: Practical Issues
Linear Order
  how to order the basic blocks linearly?
Physical registers
  how to process physical registers?
Spilling
  how to spill variables to frames?
Coalescing
  how to coalesce move-related variables?

## Slide 29
Linear Order

## Slide 30: Linearization
Linearization places basic blocks in a CFG into a linear order
  so that we can calculate live intervals
Many possible strategies
  natural order, quasi topo-sort, arbitrary, etc.
Linearization does not affect correctness, but may affect efficiency
  several examples next

## Slide 31: Example #1
L_0:
Cjmp(…, L_1, L_2);
L_1:
a = 4;
b = 3;
jmp L_3;
L_2:
a = 6;
b = 5;
jmp L_3;
L_3:
c = a+b;
return c
Cjmp(…, L_1, L_2);
a = 4;
b = 3;
jmp L_3;
a = 6;
b = 5;
jmp L_3;
c = a+b
return c
L_3
L_1
L_2
One possible quasi top-sort order.
a
b
L_0

## Slide 32: Example #1
L_0:
Cjmp(…, L_1, L_2);
L_2:
a = 6;
b = 5;
jmp L_3;
L_1:
a = 4;
b = 3;
jmp L_3;
L_3:
c = a+b;
return c
Cjmp(…, L_1, L_2);
a = 4;
b = 3;
jmp L_3;
a = 6;
b = 5;
jmp L_3;
c = a+b
return c
L_3
L_1
L_2
Another quasi top-sort order:
L_0, L_2, L_1, L_3.
a
b
L_0

## Slide 33: Example #1
L_0:
Cjmp(…, L_1, L_2);
L_3:
c = a+b;
return c
L_2:
a = 6;
b = 5;
jmp L_3;
L_1:
a = 4;
b = 3;
jmp L_3;
Cjmp(…, L_1, L_2);
a = 4;
b = 3;
jmp L_3;
a = 6;
b = 5;
jmp L_3;
c = a+b
return c
L_3
L_1
L_2
Yet another linear order:
L_0, L_3, L_2, L_1.
a
b
L_0
Notice that both ”a” and “b” are live-outs for the label “L_3”.

## Slide 34: Example #2: Loops
L_0:
sum = 0;
jmp L_1;
L_1:
x = scanf(…);
sum = sum + x;
cjmp(…,L_1, L_2);
L_2:
return sum;
sum=0;
jmp L_1;
x = scanf(…);
sum = sum + x;
cjmp(…, L_1, L_2)
return sum;
L_2
L_1
One linear order:
L_0, L_1, L_2.
sum
x
L_0
Notice that both ”a” and “b” are live-ins for the basic block L_3.

## Slide 35: Example #2: Loops
L_0:
sum = 0;
jmp L_1;
L_2:
return sum;
L_1:
x = scanf(…);
sum = sum + x;
cjmp(…,L_1, L_2);
sum=0;
jmp L_1;
x = scanf(…);
sum = sum + x;
cjmp(…, L_1, L_2)
return sum;
L_2
L_1
Yet another linear order:
L_0, L_2, L_1.
sum
x
L_0
Notice that both ”a” and “b” are live-ins for the basic block L_3.

## Slide 36: Example #2: Loops
L_1:
x = scanf(…);
sum = sum + x;
cjmp(…,L_1, L_2);
L_0:
sum = 0;
jmp L_1;
L_2:
return sum;
sum=0;
jmp L_1;
x = scanf(…);
sum = sum + x;
cjmp(…, L_1, L_2)
return sum;
L_2
L_1
Yet another linear order:
L_1, L_0, L_2.
sum
x
L_0
Notice that both ”a” and “b” are live-ins for the basic block L_3.

## Slide 37: Quasi Topo-sort Algorithm
blocks = []; // the visited basic blocks
dfs(B)
foreach(successor s of B)
if(not visited “s”)
dfs(s);
blocks += B;
topoSort(p)
dfs(p); // from the entry block
return rev(blocks);

## Slide 38
Physical Registers

## Slide 39: Physical registers
We keep track of, for each live interval i, which physical registers interference with this interval
  can be done during the construction of live intervals
During allocation, we do not allocate the target interval to interference physical registers

## Slide 40: Example
long f(long x, long y){
long a, b, c, d;
movq %rdi, x
movq %rsi, y
movq x, a
addq y, a
movq a, b
addq $4, b
movq b, %rax
imulq $2
movq %rax, c
movq c, %rax
cqto
idivq $8
movq %rax, d
movq d, %rax
ret
}
rax
rax
rax
rax, rdx
rax
c
rax
rax
b
b
a
a, y
rsi, x
x, y
d
rdi, rsi
x
y
a
b
c
d
interference registers:
x: {%rsi}
y: {}
a: {}
b: {}
c: {}
d: {}

## Slide 41
Spilling

## Slide 42: Spilling
We should generate spill code, when registers are out of supply
A possible strategy is to mark spills, rewrite code, then start over
  just like we did in the graph coloring-based allocator
  But that might be too expensive for linear scan allocators
We can use a lightweight strategy

## Slide 43: Lightweight Spilling
We reserve, among all K registers, F registers for spilling usage
  hence K-F registers left for allocation
F is the maximal #use/defs in any statements in the program
  typically, F=2 for RISC (also x64 as we used in the lab)

## Slide 44: Lightweight Spilling
When we spill a live interval i (hence its corresponding variable x):
  rewrite its use to (%r is a reserved reg):
    %r = M[l_x]
    t = %r+v
  Notice that the live interval for %r is 1
We can do it for defs
  Note that this rewriting is syntax-directed and local

## Slide 45: Lightweight Spilling
1: a = 1
2: b = 2
3: c = a+b
4: d = a+c
5: e = a+b
6: f = d+e
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
Suppose we have 4 registers:
r1, r2, r3, r4.
We reserve r3 and r4.
Variable c should be spilled, hence, rewrite its use/defs, using reserved regs.
Allocate variable e to register r1.
SP
Similarly, variable d should be spilled, rewrite its use/defs.
SP
M[l_c]=r3
r3=M[l_c]
M[l_d]=r3
r3=M[l_d]

## Slide 46: Code Rewriting
1: r1 = 1
2: r2 = 2
3: r3 = r1+r2
M[l_c]=r3
r3=M[l_c]
4: r3 = r1+r3
M[l_d]=r3
5: r2 = r1+r3
r3=M[l_d]
6: f = r3+r1
a
b
d
e
c
a: [1, 5]
b: [2, 5]
c: [3, 4]
d: [4, 6]
e: [5, 6]
Suppose we have 4 registers:
r1, r2, r3, r4.
We reserve r3 and r4.
Variable c should be spilled, hence, rewrite its use/defs.
Allocate variable e to register r1.
SP
Similarly, variable d should be spilled, hence, we rewrite its use/defs/
SP

## Slide 47
Coalescing

## Slide 48: Coalescing
Coalescing eliminates a move-related assignment by allocating the use/def to a same physical register r
We can use heuristics, for example:
  Adjacency analysis
  Move-variable analysis

## Slide 49: #1: First Match Analysis
When allocating register for a def in a move statement, for the first assignment to the variable y, as:
  y = x; or
  y = %r
We can allocate the register r for the variable x, if r has been allocated
  and %r does not interference with y
  A local and greedy heuristic

## Slide 50: Example
long f(long x, long y){
long a, b, c, d;
movq %rdi, x
movq %rsi, y
movq x, a
addq y, a
movq a, b
addq $4, b
movq b, %rax
imulq $2
movq %rax, c
movq c, %rax
cqto
idivq $8
movq %rax, d
movq d, %rax
ret
}
rax
rax
rax
rax, rdx
rax
c
rax
rax
b
b
a
a, y
rsi, x
x, y
d
rdi, rsi
x
y
a
b
c
d
1st move-related variable/reg:
x: movq
y: movq
a: movq
b: movq
c: movq
d: movq
%rdi
%rsi
%rdi
%rdi
%rax
%rax

## Slide 51: #2: Move-variable Analysis
When allocating register for a variable x, keep track of all variables that move-related to x
And allocate a register r with the highest weight
  possible weights: #occurrences, etc.

## Slide 52: Example
long f(long x, long y){
long a, b, c, d;
movq %rdi, x
movq %rsi, y
movq x, a
addq y, a
movq a, b
addq $4, b
movq b, %rax
imulq $2
movq %rax, c
movq c, %rax
cqto
idivq $8
movq %rax, d
movq d, %rax
ret
}
rax
rax
rax
rax, rdx
rax
c
rax
rax
b
b
a
a, y
rsi, x
x, y
d
rdi, rsi
x
y
a
b
c
d
Move-related variables/regs:
x: {%rdi}
y: {%rsi}
a: {x}
b: {a, %rax}
c: {%rax}
d: {%rax}
%rdi
%rsi
%rdi
%rdi
%rax
%rax

## Slide 53: Summary
Linear scan register allocation is a relatively simple, lightweight, and fast allocation algorithm
Many potential improvements and variants
  Widely used in production compilers due to its engineering advantages